## Slide 1: CSE 209 Computer Architecture Design of an ALU
Saem Hasan
Lecturer
CSE, BUET

## Slide 2: ALU and the Processor
ALU stands for Arithmetic Logic Unit
  A part of the processor or CPU

## Slide 3: Some Terminologies Revisiting
Decoder, Encoder
2X4
Decoder
E
4X2
Encoder
E

## Slide 4: Some Terminologies Revisiting
DeMUX, MUX
1X4
DeMUX
4X1
MUX

## Slide 5: A Simplified Processor in Operation
0000 0001 0010 0011

## Slide 6: Simplified Processor with Scratchpad Memory

## Slide 7: Simplified Processor with Scratchpad Memory

## Slide 8: Simplified Processor with Accumulator

## Slide 9: An ALU Unit
Can perform both Arithmetic and Logic Operations
Arithmetic/Logical Operation
Which Operation/Function
Helps Function-select to add more variants

## Slide 10: Parallel Adder
Parallel adder
  A number of full-adder circuits connected in cascade

## Slide 11: 1-bit Half Adder

## Slide 12: 1-bit Full Adder

## Slide 13: Parallel Adders
  number of 1-bit full-adders are connected in cascade to form a -bit parallel adder

## Slide 14: Arithmetic Operations by ALU

## Slide 15: Arithmetic Operations by ALU

## Slide 16: What are we doing?
Keeping A fixed and changing B to generate different operations
Changes in B
  Keeping B as it is
  Inverting all bits of B
  Changing each bit of B to 0
  Changing each bit of B to 1
Let’s assume represents modified representation of and thus represents
So, following 4 combinations can be obtained
  Keeping B as it is ()
  Inverting all bits of B ()
  Changing each bit of B to 0 ()
  Changing each bit of B to 1 ()

## Slide 17: What are we doing?
So Following 4 combinations can be obtained
  Keeping B as it is ()
  Inverting all bits of B ()
  Changing each bit of B to 0 ()
  Changing each bit of B to 1 ()
+

## Slide 18: Function Table
Modified

## Slide 19: Function Table: Designer’s perspective
Modified

## Slide 20: Function Table
Modified

## Slide 21: Logic Diagram of an independent Arithmetic Circuit
Parallel adder
Combinational Circuit
…
Selection Variables

## Slide 22: Design Example
Design an adder/subtractor circuit with one selection variable s and two inputs A and B. When s=0, the circuit performs A+B. When s=1, the circuit performs A-B by taking the 2’s complement of B.
Functions
Parallel adder
Combinational Circuit
…
Selection Variables
s | 
0 | 
1 | 
s | 
0 | 
1 | 
s | 
0 | 0
1 | 1
s | 
0 | 0
1 | 1

## Slide 23: Design Example

## Slide 24: Designing a Logic Circuit
We shall implement three basic logical operations (AND, OR and NOT) and an XOR operation

## Slide 25: Designing a Logic Circuit
Let’s combine it with arithmetic operations

## Slide 26: More Efficient Design
Use already available arithmetic circuit and incorporate logical operations
Procedure
  Design the arithmetic section independently
  Take the circuit, consider and determine which logic operations are automatically generated from the arithmetic circuit
  Modify the circuit to incorporate required but not automatically generated logic operations

## Slide 27: More Efficient Design
Use already available arithmetic circuit and incorporate logical operations

## Slide 28: More Efficient Design
Use already available arithmetic circuit and incorporate logical operations

## Slide 29: Incorporating remaining functions
Unresolved cases
 |  |  |  |  | Automatically Obtained | Required
1 | 0 | 0 |  | 0 |  | 
1 | 1 | 0 |  |  |  | 
1 | 0 | 0 |  | 0 |  | 
1 | 1 | 0 |  |  |  | 

## Slide 30: Incorporating remaining functions
(A + K)

## Slide 31: Final Boolean Functions
Combining the arithmetic and logical cases, we get the final form of the Boolean function as:
where C1 = Cin

## Slide 32: Let’s See Another Example
Derive the input equations (Xi, Yi and Zi) for the parallel adders to be used in the ALU which satisfies the following functional design specification.
s2 | s1 | cin | Required Functions
0 | 0 | 0 | F = AB + C
0 | 0 | 1 | F = AB + C + 1
0 | 1 | 0 | F = AB
0 | 1 | 1 | F = AB + 1
1 | 0 | x | F = (AB)’
1 | 1 | x | F = AB

## Slide 33: Solution
s2 | s1 | cin | X | Y | Z | Required Functions
0 | 0 | 0 | AB | C | 0 | F= AB + C
0 | 0 | 1 | AB | C | 1 | F = AB + C +1
0 | 1 | 0 | AB | 0 | 0 | F = AB
0 | 1 | 1 | AB | 0 | 1 | F = AB + 1
1 | 0 | x |  |  |  | F = (AB)’
1 | 1 | x |  |  |  | F = AB

## Slide 34: Solution
X = AB
Y = s1’ C
Z = ci
where c1 = cin

## Slide 35: Solution
s2 | s1 | cin | X | Y | Z | Required Functions
0 | 0 | 0 | AB | C | 0 | F= AB + C
0 | 0 | 1 | AB | C | 1 | F = AB + C +1
0 | 1 | 0 | AB | 0 | 0 | F = AB
0 | 1 | 1 | AB | 0 | 1 | F = AB + 1
1 | 0 | x | AB | 1 | x | F = (AB)’
1 | 1 | x | AB | 0 | x | F = AB

## Slide 36: Solution
X = AB
Y = s1’ C
Z = ci
where c1 = cin
Then for logical operations,
  X = AB
  Y = s1’ C + s2 s1’
  Z = s2’ ci

## Slide 37: Status Register
Four bits represents four status bits
  C: Contains the output carry of the operation
  S: Contains the sign of the result of the operation
  Z: Indicates whether the -bit of the result is 0 or not
  V: Indicates any overflow has occurred due to the operation
Status bits help to determine relationships among inputs
Example:
  Compare the value of A with the value of B
  Determine the value of bit of an input

## Slide 38: Status Register

## Slide 39: Comparing two unsigned numbers
  Compare the value of A with the value of B
  Check the status bits (mainly C and Z) after the performing the following operation

## Slide 40: Comparing two signed numbers
  Compare the value of A with the value of B
  Check the status bits (mainly Z, V and S) after the performing the following operation

## Slide 41: Effect of Output Carry

## Slide 42: Overflow Flag

## Slide 43: References
Digital Logic and Computer Design by M. Morris Mano
  Chapter 9 (9.1-9.7)

## Slide 44: Thank You 