## Slide 1: CSE 305 Computer Architecture Instructions
Saem Hasan
Lecturer, CSE, BUET
Prepared by
Madhusudan Basak
Assistant Professor, CSE, BUET
*Some modifications done by Saem Hasan

## Slide 2: Instructions
A computer is run by instructions
Instruction Set
  All possible instructions for a CPU

## Slide 3: Instruction Set Architecture
Instruction set architecture is the attributes of a computing system as seen by the assembly language programmer or compiler.
  Instruction Set (what operations can be performed?)
  Instruction Format (how are instructions specified?)
  Data storage (where is data located?)
  Addressing Modes (how is data accessed?)
  Exceptional Conditions (what happens if something goes wrong?)

## Slide 4: Design Philosophy

## Slide 5: MIPS Architecture
Acronym of “Microprocessor without Interlocked Pipelined Stages”
  Is a RISC (Reduced Instruction Set Computer) ISA (Instruction Set Architecture)
  Developed by MIPS Technologies (then MIPS Computer Systems) in 1985

## Slide 6: Design Principles
Design Principle 1: Simplicity favors regularity.
Design Principle 2: Smaller is faster.
Design Principle 3: Good design demands good compromises.

## Slide 7: Simplicity favors regularity
The instructions of MIPS are fixed and rigid
Rigidity ensures Regularity
Simplicity favors regularity

## Slide 8: Example Instruction
and instructions always follow the following fixed format

## Slide 9: Example Instruction
and instructions always follow the following fixed format

## Slide 10: MIPS Instruction Properties
Arithmetic operations only takes register values as operands
Size of a register : 32 bit
Number of registers: 32
  Satisfies Design Principle 2: Smaller is faster.
    Large number of registers -> longer time for electronic signal to travel -> Increased clock cycle
    Large number of registers -> Increased number of control bits
A number is dedicated to a particular register.
  5 bit are reserved to indicate each register when the count is 32
  Compiler maps a program variable to a register
  There is a number assigned against each register

## Slide 11: MIPS Instruction Properties
Example

## Slide 12: MIPS Instruction Properties
What about data structures (Arrays and Structures)?
  These are kept in memory and a particular element is transferred to registers whenever required
Compiler
  places an array/structure into memory
  keeps the starting address of the memory in a register
  tracks which register is used for which array/structure
Data Transfer Instructions
  load word:
  store word:

## Slide 13: Data Transfer Instructions
Example

## Slide 14: Spilling Registers
What if the number of variables and data structures is more than 32?
  ﻿The process of putting less commonly used variables into memory is called Spilling Registers.
  Keeps the most frequently used variables in registers and less frequents one in memory
  Moves variables around registers and memory

## Slide 15: Operation with Constants
Add immediate or addi instruction
  Takes one register and one constant as input
Constant 0 is used very often (e.g., for transfer operations)
  A register is dedicated for this purpose
  #$s2=$s3
Is an instruction represented using register names?

## Slide 16: Representing Instructions in the Computer
Key principles of Today’s computer instructions
  Instructions are represented as numbers
  Program are stored in memory to be read or written, just like data

## Slide 17: Representing Instructions in the Computer
An instruction is a sequence of bits
Each register is mapped to a number
  There is a convention to map register names into numbers (e.g., registers $s0 to $s7 map onto registers 16 to 23)
Each instruction is 32 bit long (size of a word)
  Satisfies Design Principle 1: Simplicity favors regularity.
Instruction Format: format used by an instruction

## Slide 18: An MIPS Instruction Format
R-Format
  Deals with arithmetic operations with registers
  shorthand of opcode, denotes operation type and format type
  Source Register1
  Source Register 2
  Destination Register
  Shorthand of shift amount
  shorthand of function code, denotes the specific variant of an operation

## Slide 19: An MIPS Instruction Format
Would it be good to use just one format for all kind of operations?
No!
Design Principle 3: Good design demands good compromises.

## Slide 20: Another MIPS Instruction Format
I-Format
  Deals with immediate and data transfer operations
  Here represents the destination register

## Slide 21: MIPS Instruction Encoding (Simplified)

## Slide 22: Summary

## Slide 23: Logical Operations
No NOT Operation?

## Slide 24: Shift Left
sll $t2,$s0,4 # reg $t2 = reg $s0 << 4 bits

## Slide 25: Branching Operations
if (i==j)
f = g + h;
else
f = g – h;
Why not blt?

## Slide 26: Branching Operations

## Slide 27: Memory Allocation for Program and Data
Reserved Memory
Text Segment: Program Code
Static Data Segment:
  Contains static variables, constants, arrays
Dynamic Data Segment (Heap):
  Contains linked lists, variable length data
Stack
  Contains function local variables, parameters etc.

## Slide 28: Stack During Procedure Call
Stores/saves the values of registers and Restores those later
Either $sp and $fp combination, or only $sp is used
The allocated stack area by a procedure is known as activation record or procedure frame

## Slide 29: Stack During Procedure Call
Stores the values of registers

## Slide 30: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.

## Slide 31: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.
Place for parameters:
  $a0–$a3: four argument registers in which to pass parameters
  Memory (e.g., stack) can be used if more values to be passed

## Slide 32: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.
Transfer Control:
  Jump-and-link instruction (jal)
  Keeps the return address for the procedure in $ra and jumps to the

## Slide 33: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.
Acquiring the storage resources
  Different register values (manipulated by caller) are stored in the stack
  Prepares the registers for operations
  Can use the memory for data storage

## Slide 34: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.

## Slide 35: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.
Performing Tasks
  Can perform all the operations allowed by the MIPS instruction set

## Slide 36: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.
Result storing by the callee
  $v0–$v1: two value registers in which to return values
  Memory (e.g., stack) can be used if more values to be returned

## Slide 37: Procedures in MIPS
Six steps during a procedure call
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure.
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.
Procedure returned
  Stack is adjusted using $sp and $fp pointers
  An unconditional jump to the address from where the caller will resume execution

## Slide 38: An Example
non_leaf:
  ...
  add $a0, $s1, $zero
  add $a1, $s2, $zero
  add $a2, $s3, $zero
  add $a3, $s4, $zero
  jal leaf
  add $s1, $zero, $v0
  ...
leaf: addi $sp, $sp, –12 # adjust stack to make room for 3 items
  sw $t1, 8($sp) # save register $t1 for use afterwards
  sw $t0, 4($sp) # save register $t0 for use afterwards
  sw $s0, 0($sp) # save register $s0 for use afterwards
  add $t0,$a0,$a1 # register $t0 contains g + h
  add $t1,$a2,$a3 # register $t1 contains i + j
  sub $s0,$t0,$t1 # f = $t0 – $t1, which is (g + h)–(i + j)
  add $v0,$s0,$zero # Set return Value
  lw $s0, 0($sp) # restore register $s0 for caller
  lw $t0, 4($sp) # restore register $t0 for caller
  lw $t1, 8($sp) # restore register $t1 for caller
  addi $sp,$sp,12 # adjust stack to delete 3 items
  jr $ra # jump back to calling routine
  Put parameters in a place where the procedure can access them.
  Transfer control to the procedure.
  Acquire the storage resources needed for the procedure
  Perform the desired task.
  Put the result value in a place where the calling program can access it.
  Return control to the point of origin, since a procedure can be called from several points in a program.

## Slide 39: Nested Call
fact: addi $sp, $sp, –8 # adjust stack for 2 items
  sw $ra, 4($sp) # save the return address
  sw $a0, 0($sp) # save the argument n
  slti $t0,$a0,1 # test for n < 1
  beq $t0,$zero,L1 # if n >= 1, go to L1
  addi $v0,$zero,1 # Set the return value
  addi $sp,$sp,8 # pop 2 items off stack
  jr $ra # return to caller
L1: addi $a0,$a0,–1 # n >= 1: argument gets (n – 1)
  jal fact # call fact with (n –1)
  lw $a0, 0($sp) # return from jal: restore argument n
  lw $ra, 4($sp) # restore the return address
  addi $sp, $sp, 8 # adjust stack pointer to pop 2 items
  mul $v0,$a0,$v0 # return n * fact (n – 1)
  jr $ra # return to the caller

## Slide 40: J-Format
To support long jump to a remote procedure address
opcode
Jumping Address

## Slide 41: ASCII representation of characters
ASCII stands for American Standard Code for Information Interchange
Uses 1 byte to represent a character

## Slide 42: 1 Byte Memory Operation
ASCII demands 1-byte memory operation
MIPS supports
lb $t0,0($sp) #Reads 1 byte from memory and stores in the lowest (rightmost) byte of $t0
sb $t0,0($gp) #Reads 1 byte from the lowest (rightmost) byte of $t0 and stores in the memory
Unsigned Version:
Load Byte: lbu
Store Byte: Not available in MIPS

## Slide 43: Dealing with Strings
Three commonly available strategies
  the first position of the string is reserved to give the length of a string
  an accompanying variable has the length of the string
  the last position of a string is indicated by a character used to mark the end of a string

## Slide 44: Dealing with String: Example
ASCII demands 1-byte memory operation
MIPS supports
lb $t0,0($sp) #Reads 1 byte from memory and stores in the lowest (rightmost) byte of $t0
sb $t0,0($gp) #Reads 1 byte from the lowest (rightmost) byte of $t0 and stores in the memory
Unsigned Version:
Load Byte: lbu
Store Byte: Not available in MIPS

## Slide 45: Dealing with String: An Example
strcpy: addi $sp,$sp,–4 # adjust stack for 1 more item
sw $s0, 0($sp) # save $s0
add $s0,$zero,$zero # i = 0 + 0
L1: add $t1,$s0,$a1 # address of y[i] in $t1
lbu $t2, 0($t1) # $t2 = y[i]
add $t3,$s0,$a0 # address of x[i] in $t3
sb $t2, 0($t3) # x[i] = y[i]
beq $t2,$zero,L2 # if y[i] == 0, go to L2
addi $s0, $s0,1 # i = i + 1
j L1 # go to L1. While loop continues
L2: lw $s0, 0($sp) # End of string. Restore old $s0
addi $sp,$sp,4 # pop 1 word off stack
jr $ra # return

## Slide 46: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 47: Dealing with Multiple Languages
Unicode, a universal encoding, supports alphabets of most human languages
Java uses Unicode
Requires 16 bits to represent a character
Operations required to load and store 16bits (halfwords)
  Load halfword: lh
  Load halfword unsigned: lhu
  Store halfword: sh

## Slide 48: Constant Size: Is larger feasible?
The I-format is used by both immediate and memory data transfer operations
More than 16 bit long constant?
  We have two options in hand
    Supporting short constant in 1 instruction and deal long constant with additional instructions
    Supporting long constant in 2 instructions
  We opted for the first option (to exploit the benefit of common case fast)
Are we limited to use 16 bit constants (-32,768 to 32,767)?
No  Use two instructions to populate a register with 32 bit constant

## Slide 49: Manipulating Larger Constant
Populating a register with 32 bit constant
  Load Upper Immediate (lui) : Loads upper 16 bits
  Or Immediate (ori): : Loads lower 16 bits
Example: x=y+4000000
4000000 = 0000 0000 0011 1101 0000 1001 0000 0000
lui $s0, 61 // 61 = 0000 0000 0011 1101
ori $s0, 2304 // 2304= 0000 1001 0000 0000
add $s1, $t0, $s0
Think how to use 32 bit address to access data from memory
0000 0000 0011 1101
0000 0000 0000 0000
0000 0000 0000 0000
0000 1001 0000 0000
No sign extension for logical operations but it happens for arithmetic operations
$s0
0000 1001 0000 0000

## Slide 50: Addressing in Branches
PC is 32 bit but the address in conditional branching (if-else, loop etc.) is16 bit
  Forces the program instruction count within instructions (Bytes=128 KB)
Most of the conditional branches jump nearby (weather forward or backward)
Use PC relative addressing to access forward (PC + relative constant address), or backward (PC – relative constant address) location
Can support branching up to relative constant address value
PC normally increments 1 word (4 bytes) after every instruction
The addressing should be (PC+4 + relative constant address) for forward access and (PC + 4 – relative constant address) for backward access

## Slide 51: Addressing in Jumps
PC is 32 bit but the address in Jumps is16 bit
  Forces the program instruction count within instructions ()
opcode
Jumping Address

## Slide 52: Addressing in Jumps
PC is 32 bit but the address in Jumps is16 bit
  Forces the program instruction count within instructions ()
Replaces the 28 rightmost byte of PC
  Known as pseudodirect addressing
  A program is not placed across an address boundary of 256 MB
  Otherwise, a jump must be replaced by a jump register instruction preceded by other instructions to load the full 32-bit address into a register
opcode
Jumping Address

## Slide 53: Food for Thought
Can you reverse engineer a binary?
Is your IP secured?

## Slide 54: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 55: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5,Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 56: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
  beq $s0,$s1, L1
  ↓
  bne $s0,$s1, L2 j L1 L2: …

## Slide 57: Addressing Mode Summary

## Slide 58: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization

## Slide 59: Synchronization in MIPS
Load linked: ll rt, offset(rs)
Store conditional: sc rt, offset(rs)
  Succeeds if location not changed since the ll
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: add $t0,$zero,$s4 ;copy exchange value
  ll $t1,0($s1) ;load linked
  sc $t0,0($s1) ;store conditional
  beq $t0,$zero,try ;branch store fails
  add $s4,$zero,$t1 ;put load value in $s4
Notes: The idea is that you use LL to load the value stored at a memory location into a register, modify it however you like there, and subsequently write it back to the same place using SC. SC will only overwrite the value in memory with your modified one if no other processor has altered it while you were working on the copy in the register. It has the side-effect of setting a status flag to indicate whether or not it was successful.

## Slide 60: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 61: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary

## Slide 62: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 63: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 64: Object 1

## Slide 65: Object 2

## Slide 67: Merged Object

## Slide 68: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall

## Slide 69: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 70: Dynamically Linked Libraries (DLL)
Library routines that are linked to a program during execution
  To incorporate the updated version of library routines
In lazy procedure linkage, each routine is linked only when it is called
  Provides a level of indirection
  Nonlocal routine calls a set of dummy entries at the end of the program, with one entry per nonlocal routine. These dummy entries each contain an indirect jump
  The Dynamic Linker/Loader finds the desired routine, remaps it, and changes the address in the indirect jump location to point to that routine
  From then, the call to the library routine jump indirectly to routine without the extra hops

## Slide 71: Lazy Linkage
Indirection table
Stub: Loads routine ID, Jump to linker/loader
Linker/loader code
Dynamically mapped code

## Slide 72: Starting a Java Program
Java programs ensure portability sacrificing some performance
Compiled first in to an easy-to-interpret instruction set: Java bytecode
A software interpreter, called Java Virtual Machine (JVM) can execute Java byte code
  This process is slow
Just In Time Compiler (JIT) makes it faster
  Statistically identify the commonly used (hot) methods
  Compiles these methods into native instruction set

## Slide 73: Starting Java Applications
Simple portable instruction set for the JVM
Interprets bytecodes
Compiles bytecodes of “hot” methods into native code for host machine

## Slide 74: C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in $a0, k in $a1, temp in $t0
§2.13 A C Sort Example to Put It All Together

## Slide 75: The Procedure Swap
swap: sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4)
# (address of v[k])
lw $t0, 0($t1) # $t0 (temp) = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0 (temp)
jr $ra # return to calling routine

## Slide 76: The Sort Procedure in C
Non-leaf (calls swap)
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;
  j >= 0 && v[j] > v[j + 1];
  j -= 1) {
  swap(v,j);
  }
  }
  }
  v in $a0, k in $a1, i in $s0, j in $s1

## Slide 77: The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine

## Slide 78: The Procedure Body
move $s2, $a0 # save $a0 into $s2
move $s3, $a1 # save $a1 into $s3
move $s0, $zero # i = 0
for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 ≥ $s3 (i ≥ n)
beq $t0, $zero, exit1 # go to exit1 if $s0 ≥ $s3 (i ≥ n)
addi $s1, $s0, –1 # j = i – 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
sll $t1, $s1, 2 # $t1 = j * 4
add $t2, $s2, $t1 # $t2 = v + (j * 4)
lw $t3, 0($t2) # $t3 = v[j]
lw $t4, 4($t2) # $t4 = v[j + 1]
slt $t0, $t4, $t3 # $t0 = 0 if $t4 ≥ $t3
beq $t0, $zero, exit2 # go to exit2 if $t4 ≥ $t3
move $a0, $s2 # 1st param of swap is v (old $a0)
move $a1, $s1 # 2nd param of swap is j
jal swap # call swap procedure
addi $s1, $s1, –1 # j –= 1
j for2tst # jump to test of inner loop
exit2: addi $s0, $s0, 1 # i += 1
j for1tst # jump to test of outer loop
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 79: Example: Clearing and Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2

## Slide 80: Comparison of Array vs. Ptr
Multiply “strength reduced” to shift
Array version requires shift to be inside loop
  Part of index calculation for incremented i
  c.f. incrementing pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer

## Slide 81: MIPS (RISC) Design Principles In Summary
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers
  limited number of addressing modes
Good design demands good compromises
  Three instruction formats
Make the common case fast
  arithmetic operands using the registers
  Saving the commonly used registers into stack
  PC-relative addressing
  allow instructions to contain immediate operands

## Slide 82: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux

## Slide 83: Effect of Language and Algorithm

## Slide 84: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 85: Alternative Architectures
Design alternative
  provide more powerful operations
  goal is to reduce number of instructions executed
  danger is a slower cycle time and/or a higher CPI

## Slide 86: ARM & MIPS Similarities
ARM: the most popular embedded core
Similar basic set of instructions to MIPS
§2.16 Real Stuff: ARM Instructions
 | ARM | MIPS
Date announced | 1985 | 1985
Instruction size | 32 bits | 32 bits
Address space | 32-bit flat | 32-bit flat
Data alignment | Aligned | Aligned
Data addressing modes | 9 | 3
Registers | 15 × 32-bit | 31 × 32-bit
Input/output | Memory mapped | Memory mapped

## Slide 87: Compare and Branch in ARM
Uses condition codes for result of an arithmetic/logical instruction
  Negative, zero, carry, overflow
  Compare instructions to set condition codes without keeping the result
Each instruction can be conditional
  Top 4 bits of instruction word: condition value
  Can avoid branches over single instructions

## Slide 88: Instruction Encoding

## Slide 89: The Intel x86 ISA
Evolution with backward compatibility
  8080 (1974): 8-bit microprocessor
    Accumulator, plus 3 index-register pairs
  8086 (1978): 16-bit extension to 8080
    Complex instruction set (CISC)
  8087 (1980): floating-point coprocessor
    Adds FP instructions and register stack
  80286 (1982): 24-bit addresses, MMU
    Segmented memory mapping and protection
  80386 (1985): 32-bit extension (now IA-32)
    Additional addressing modes and operations
    Paged memory mapping as well as segments
§2.17 Real Stuff: x86 Instructions

## Slide 90: The Intel x86 ISA
Further evolution…
  i486 (1989): pipelined, on-chip caches and FPU
    Compatible competitors: AMD, Cyrix, …
  Pentium (1993): superscalar, 64-bit datapath
    Later versions added MMX (Multi-Media eXtension) instructions
    The infamous FDIV bug
  Pentium Pro (1995), Pentium II (1997)
    New microarchitecture (see Colwell, The Pentium Chronicles)
  Pentium III (1999)
    Added SSE (Streaming SIMD Extensions) and associated registers
  Pentium 4 (2001)
    New microarchitecture
    Added SSE2 instructions

## Slide 91: The Intel x86 ISA
And further…
  AMD64 (2003): extended architecture to 64 bits
  EM64T – Extended Memory 64 Technology (2004)
    AMD64 adopted by Intel (with refinements)
    Added SSE3 instructions
  Intel Core (2006)
    Added SSE4 instructions, virtual machine support
  AMD64 (announced 2007): SSE5 instructions
    Intel declined to follow, instead…
  Advanced Vector Extension (announced 2008)
    Longer SSE registers, more instructions
If Intel didn’t extend with compatibility, its competitors would!
  Technical elegance ≠ market success

## Slide 92: Basic x86 Registers

## Slide 93: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement

## Slide 94: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …

## Slide 95: Implementing IA-32 (Seg:Off)
Complex instruction set makes implementation difficult
  Hardware translates instructions to simpler microoperations
    Simple instructions: 1–1
    Complex instructions: 1–many
  Microengine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid complex instructions

## Slide 96: ARM v8 Instructions
In moving to 64-bit, ARM did a complete overhaul
ARM v8 resembles MIPS
  Changes from v7:
    No conditional execution field
    Immediate field is 12-bit constant
    Dropped load/store multiple
    PC is no longer a GPR
    GPR set expanded to 32
    Addressing modes work for all word sizes
    Divide instruction
    Branch if equal/branch if not equal instructions
§2.18 Real Stuff: ARM v8 (64-bit) Instructions

## Slide 97: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.19 Fallacies and Pitfalls

## Slide 98: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 99: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 100: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises
Layers of software/hardware
  Compiler, assembler, hardware
MIPS: typical of RISC ISAs
  c.f. x86
§2.20 Concluding Remarks

## Slide 101: Concluding Remarks
Measure MIPS instruction executions in benchmark programs
  Consider making the common case fast
  Consider compromises
Instruction class | MIPS examples | SPEC2006 Int | SPEC2006 FP
Arithmetic | add, sub, addi | 16% | 48%
Data transfer | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36%
Logical | and, or, nor, andi, ori, sll, srl | 12% | 4%
Cond. Branch | beq, bne, slt, slti, sltiu | 34% | 8%
Jump | j, jr, jal | 2% | 0%

## Slide 102: Acknowledgements
These slides contain material developed and copyright by:
  Lecture slides by Dr. Tanzima Hashem, Professor, CSE, BUET
  Lecture slides by Mehnaz Tabassum Mahin, Assistant Professor, CSE, BUET

## Slide 103: Thank You 