## Slide 1: CSE 205: Digital Logic Design

## Slide 2: Textbook
Digital Design (5th Edition)
  M. Morris Mano
  Michael D. Ciletti

## Slide 3: Digital Systems
Why study digital logic design
  To design and build a digital system
Digital Systems
  Example: digital cameras, digital telephones, digital television, digital computers…
  Used in communication, business transactions, traffic control, space guidance, medical treatment, weather monitoring, the Internet …

## Slide 4: Binary Logic
In a digital system, all signals take on discrete values.
  Also referred as states
Most modern digital systems operate on 2 discrete states
  Binary logic system
    Deals with binary variables and a set of logical operations

## Slide 5: Binary Logic
We represent the two states of binary variable as
  True and false
  1 and 0
  High and Low
Three basic logic operations
  AND: x.y = z or xy = z
  OR: x + y = z
  NOT: x’ = z or x = z

## Slide 6: Truth Table
Specifies results for all possible input combinations

## Slide 7: Logic Gates
Logic gates are electronic circuits that operate on one or more input signals to produce an output signal.

## Slide 8: Logic Gates

## Slide 9
Logic Gates

## Slide 10: Boolean Function
An algebraic expression
  Binary variables
  Constants 0 and 1
  Logic operation symbols
f(x,y,z) = (x + y’)z + x’
Some terminology, notation and precedence:
  f is the name of the function.
  (x,y,z) are the input variables, each representing 1 or 0.
  A literal is a single variable within a term, in complemented or uncomplemented form. The function above has four literals: x, y’, z, and x’.
  Parenthesis has the highest precedence, followed by NOT, AND, and then OR.

## Slide 11: Gate Implementation of a Function

## Slide 12: Gate Implementation of a Function
f(x,y,z) = x’ + y
x
x+y

## Slide 13: Gate Implementation of a Function
f(x,y,z) = (x + y)x
_______
x+y
x+y
(x+y)x

## Slide 14: Boolean Function
A Boolean function can be represented in a truth table.
f(0,0,0) = (0 + 1)0 + 1 = 1
f(0,0,1) = (0 + 1)1 + 1 = 1
f(0,1,0) = (0 + 0)0 + 1 = 1
f(0,1,1) = (0 + 0)1 + 1 = 1
f(1,0,0) = (1 + 1)0 + 0 = 0
f(1,0,1) = (1 + 1)1 + 0 = 1
f(1,1,0) = (1 + 0)0 + 0 = 0
f(1,1,1) = (1 + 0)1 + 0 = 1
f(x,y,z) = (x + y’)z + x’

## Slide 15: Boolean Function
A Boolean function can be represented in a truth table.

## Slide 16: Number Systems
Consists of TWO Things:
  A BASE or RADIX Value
  A SET of DIGITS
    Digits are symbols representing all values less than the radix value.
Example is the Common Decimal System:
  RADIX (BASE) = 10
  Digit Set = {0, 1, 2, 3, 4, 5, 6, 7, 8, 9}

## Slide 17: Decimal Number Systems
Consider: 5032.21
Other Notation: (5032.21)10
In general, a number expressed in a base-r system has coefficients multiplied by powers of r:
a
n n-1 1 0 -1 -2 -m
r +a
n
r +…+a
n-1
r +a
1
+a
r +a
-1
r +…+a
-2
r
-m

## Slide 18: Other Number Systems
Binary
  Radix = (2)10
  Digit Set = {0,1}
Octal
  Radix = (8)10
  Digit Set = {0,1,2,3,4,5,6,7}
Hexadecimal
  Radix = (16)10
  Digit Set = {0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F}

## Slide 19: Binary Number Systems
Binary
  Radix = (2)10
  Digit Set = {0,1}
Binary to Decimal:

## Slide 20: Binary to Decimal: practice
0110 2 = ?
11010 2 = ?
0110101 2 = ?
11010011 2 = ?
26 10
53 10
211 10
6 10

## Slide 21: Octal Number Systems
Octal
  Radix = (8)10
  Digit Set = {0,1,2,3,4,5,6,7}
Octal to Decimal:

## Slide 22: Hexadecimal Number Systems
Hexadecimal
  Radix = (16)10
  Digit Set = {0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F}
Hexadecimal to Decimal:

## Slide 23: Decimal (Integer) to Binary
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division
Example: (13)10
Quotient
Remainder
Coefficient
Answer: (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB
13
/ 2 = 6
1 a0 = 1
6
/ 2 = 3
0 a1 = 0
3
/ 2 = 1
1 a2 = 1
1
/ 2 = 0
1 a3 = 1

## Slide 24: Decimal to binary: practice
1310 = ?
2210 = ?
4310 = ?
15810 = ?
1 0 1 1 0 2
1 0 1 0 1 1 2
1 0 0 1 1 1 1 0 2
1 1 0 1 2

## Slide 25: Decimal (Fraction) to Binary
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division
Example: (0.625)10
Integer
Fraction
Coefficient
Answer: (0.625)10 = (0.a-1 a-2 a-3)2 = (0.101)2
MSB LSB
0.625
* 2 = 1 . 25
0.25
* 2 = 0 . 5 a-2 = 0
0.5
* 2 = 1 . 0 a-3 = 1
a-1 = 1

## Slide 26: Decimal to Octal Conversion
Example: (175)10
Quotient
Remainder
Coefficient
Answer: (175)10 = (a2 a1 a0)8 = (257)8
175
/ 8 = 21
7 a0 = 7
21
/ 8 = 2
5 a1 = 5
2
/ 8 = 0
2 a2 = 2
Example: (0.3125)10
Integer
Fraction
Coefficient
Answer: (0.3125)10 = (0.a-1 a-2 a-3)8 = (0.24)8
0.3125
* 8 = 2 . 5
0.5
* 8 = 4 . 0 a-2 = 4
a-1 = 2

## Slide 27: Binary − Octal Conversion
8 = 23
Each group of 3 bits represents an octal digit
Octal | Binary
0 | 0 0 0
1 | 0 0 1
2 | 0 1 0
3 | 0 1 1
4 | 1 0 0
5 | 1 0 1
6 | 1 1 0
7 | 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 2 6 . 2 )8
Assume Zeros
Works both ways (Binary to Octal & Octal to Binary)

## Slide 28: Binary − Hexadecimal Conversion
16 = 24
Each group of 4 bits represents a hexadecimal digit
Hex | Binary
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
A | 1 0 1 0
B | 1 0 1 1
C | 1 1 0 0
D | 1 1 0 1
E | 1 1 1 0
F | 1 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Binary to Hex & Hex to Binary)

## Slide 29: Octal − Hexadecimal Conversion
Convert to Binary as an intermediate step
Example:
( 0 1 0 1 1 0 . 0 1 0 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Octal to Hex & Hex to Octal)
( 2 6 . 2 )8
Assume Zeros

## Slide 30: Binary Addition
1
0
1
1
1
1
1
1
1
1
0
+
0
0
0
0
1
1
1
≥ (2)10
1
1
1
1
1
1
= 61
= 23
= 84

## Slide 31: Binary Subtraction
0
0
1
1
1
0
1
1
1
1
0
−
0
1
0
1
1
1
0
= (10)2
2
2
2
2
1
0
0
0
1
= 77
= 23
= 54

## Slide 32: Complements
They are used to simplify the subtraction operation
Two types (for each base-r system)
  Diminishing radix complement (r-1’s complement)
  Radix complement (r’s complement)
For n-digit number N
r-1’s complement
r’s complement

## Slide 33: Diminished Radix Complement
Example for 6-digit decimal numbers:
  9’s complement is (rn – 1)–N = (106–1)–N = 999999–N
  9’s complement of 546700:
  999999–546700 = 453299
Example for 7-digit binary numbers:
  1’s complement is (rn – 1) – N = (27–1)–N = 1111111–N
  1’s complement of 1011000:
  1111111–1011000 = 0100111

## Slide 34: Radix Complement
The r's complement of an n-digit number N in base r is defined as rn – N for N ≠ 0 and as 0 for N = 0.
The r's complement can also be obtained by adding 1 to the (r  1) 's complement, since
rn – N = [(rn  1) – N] + 1.
Decimal Number: 10n - N
  Example: 10’s complement of 246700 is 753300

## Slide 35: Radix Complement (Binary Number)
Take 1’s complement then add 1
OR
Toggle all bits to the left of the first ‘1’ from the right
Example:
0 1 0 1 0 0 0 0
1 0 1 1 0 0 0 0
0 1 0 0 1 1 1 1
+ 1
1 0 1 1 0 0 0 0
0
0
0
0
1
0
1
0

## Slide 36: Subtraction with Complements
M – N
  Add M to r’s complement of N
    Sum = M+(rn – N) = M – N+ rn
  If M > N, Sum will have an end carry rn , discard it
  If M<N, Sum will not have an end carry and
    Sum = rn – (N – M) (r’s complement of N – M)
    So M – N = – (r’s complement of Sum)

## Slide 37
65438 - 5623
65438
10’s complement of 05623 +94377
159815
Discard end carry 105 -100000
Answer 59815
Subtraction with Complements

## Slide 38
5623 - 65438
Subtraction with Complements
05623
10’s complement of 65438 +34562
40185
There is no end carry.
Therefore, the answer is:
– (10's complement of 40185) =  59815.

## Slide 39
10110010 - 10011111
Subtraction with Complements
10110010
2’s complement of 10011111 +01100001
100010011
Discard end carry 2^8 - 100000000
Answer 00010011

## Slide 40
10011111 -10110010
Subtraction with Complements
10011111
2’s complement of 10110010 +01001110
11101101
Therefore, the answer is
Y – X =  (2's complement of 11101101) =  00010011.
There is no end carry.

## Slide 41: Subtraction with Complements
Subtraction of unsigned numbers can also be done by means of the (r  1)'s complement.
Remember that the (r  1) 's complement is one less then the r's complement.
10110010 - 10011111
10110010
1’s complement of 10011111 +01100000
100010010
End-around carry + 1
Answer 00010011

## Slide 42
10011111 -10110010
Subtraction with Complements
10011111
1’s complement of 10110010 +01001101
11101100
Therefore, the answer is
Y – X =  (1's complement of 11101100) =  00010011.
There is no end carry.

## Slide 43: Signed Binary Numbers
To represent negative integers, we need a notation for negative values.
It is customary to represent the sign with a bit placed in the leftmost position of the number since binary digits.
The convention is to make the sign bit 0 for positive and 1 for negative.
Example:

## Slide 44: Signed Binary Numbers Arithmetic Addition
+ 5 00000101
+11 00001011
+16 00010000
- 5 11111011
+11 00001011
+6 100000110
Discard
+ 5 00000101
-11 11110101
-6 11111010
- 5 11111011
-11 11110101
-16 111110000
Discard

## Slide 45: Signed Binary Numbers Arithmetic Subtraction
In 2’s-complement form:
Example:
Take the 2’s complement of the subtrahend (including the sign bit) and add it to the minuend (including sign bit).
A carry out of sign-bit position is discarded.
( 6)  ( 13)
(11111010  11110011)
(11111010 + 00001101)
00000111 (+ 7)

## Slide 46: Binary Codes
Generally Two Types:
Alphanumeric Codes: ASCII Code (7-bit)
EBCDIC Code (8-bit)
Numeric Codes: Weighted and Un-Weighted
Weighted Codes: 8-4-2-1, 2-4-2-1, 3-3-2-1, etc
Un-Weighted Codes: Excess-3 and Gray Codes (reflected binary code (RBC))
Alphanumeric Codes
Numeric Codes

## Slide 47: Binary Code: BCD Code
A number with k decimal digits will require 4k bits in BCD.
A decimal number in BCD is the same as its equivalent binary number only when the number is between 0 and 9.

## Slide 48: Binary Code: BCD Code
BCD Addition

## Slide 49: Binary Code: BCD Code
Example:
  Consider the addition of 184 + 576 = 760 in BCD:

## Slide 50: Binary Code: BCD Code
Decimal Arithmetic: (+375) + (-240) = +135

## Slide 51: Binary Codes Other decimal codes

## Slide 52: Binary Code: Gray Code

## Slide 53: Binary Codes: ASCII Character Code
American Standard Code for Information Interchange (Refer to Table 1.7)
A popular code used to represent information sent as character-based data.
It uses 7-bits to represent:
  94 Graphic printing characters.
  34 Non-printing characters.
Some non-printing characters are used for text format (e.g. BS = Backspace, CR = carriage return).
Other non-printing characters are used for record marking and flow control (e.g. STX and ETX start and end text areas).

## Slide 54: Binary Codes: ASCII Character Code

## Slide 55: Binary Codes: Error-Detecting Code
To detect errors in data communication and processing, an eighth bit is sometimes added to the ASCII character to indicate its parity.
A parity bit is an extra bit included with a message to make the total number of 1's either even or odd.
Example:
  Consider the following two characters and their even and odd parity:

## Slide 56: Logic Gates
Figure 2.5 Digital logic gates

## Slide 57
Figure 2.5 Digital logic gates
Logic Gates

## Slide 58: Practice: Truth table to Boolean Function
  F = xyz + xyz’+ x'yz + x'yz’
  = y
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 59: Syllabus
Chapter 1 (Excluding Section 1.8)